back

Print

# DeLonghi ECAM 656.85.MS Coffee outlet

Posted by: DocKaffee December 27, 2019 09:31 am

Recently, coffee has started to leak out behind the coffee spout next to the LED for cup lighting. The outlet itself is free. (cleaned with brush, helped at first) . How can the coffee outlet be cleaned or dismantled?

Posted by: Steinhaeger666 December 29, 2019 05:23 pm

Hello,

I'm not sure this guy's okay. But look up behind the coffee spout. Possibly there is a Phillips screw there.

If you remove these, you can pull the complete outlet forward and then disassemble and clean it. If there is no screw there, you have to remove the side parts and possibly also the top part to

be able to

remove the outlet

. VGBernd

Posted by: DocKaffee December 30, 2019 11:27 am

Thanks helped.

I didn't want to send the plane across the Republic because of a suspected blockage.

That's why I

took the plunge. All is well in hand.

1. There is a Phillips screw from below in the cup lighting. After removing this, the coffee spout can

be pulled out

to the front

.

2. To disassemble, remove the 4 screws (2 above, 1 below, 1 in the middle), push the grid in the middle to the side and

pull off

the front panel

.

3. remove chrome-plastic parts upwards and downwards. Metal bars

out the top.

However, the fault was not a blockage but a crack in the bend of the drain hose.

Bean2cup.org > DeLonghi > DeLonghi ECAM 656.85.MS Coffee outlet

#### www.bean2cup.org

back

Print