back

Print

# Melitta Avanza 600 / F270 drain valve replacement

Posted by: Moerchen February 11, 2024 12:33 pm

Hello dear community

Problem: Grinding works, but water runs into the drip tray and not through the coffee powder.

Attempts to solve the problem:

I have now taken my Melitta Avanza apart twice and cleaned it properly and descaled it where I could. Unfortunately, the problem still persists.

As I read here in the forum, the next solution is probably to replace the drain valve. Unfortunately, I can't find any information on various sites about how to have this valve delivered to Switzerland, and I'm not sure whether it will fit my Melitta. Does anyone know whether these drainage valves for Melitta coffee machines are all the same and would be compatible with mine?

Many thanks and best regards

Moerchen

Posted by: Schlawi February 11, 2024 03:43 pm

This would fit and is also delivered to Switzerlandhttps://www.ebay.ch/itm/144691873105?hash=item21b04ec551:g:A88AAOSwR4peCe4x

https://www.air-care.ch/Ablaufventil-Melitta-6769602-Drainageventil-fuer-Kaffeemaschine-Kaffeeautomat

https://www.air-care.ch/Ablaufventil-Melitta-6769602-Drainageventil-fuer-Kaffeemaschine-Kaffeeautomat

Posted by: Moerchen February 11, 2024 07:08 pm

All right, thank you Schlawi

If I understand correctly, this number is 6769602.

Is that correct?

Posted by: Schlawi February 11, 2024 07:20 pm

Exactly. You can enter your machine at various dealers (Komtra, BND) and then look for the spare part number. There are several more numbers. The valve also fits some Nivona and Miele machines. When installing, also make sure that you install the lower part correctly. The longer bar on the inside.

Posted by: Moerchen February 11, 2024 10:38 pm

Great!

I even found a dealer in Switzerland who has it in stock for the number 6769600 and will try my luck there.

https://fixpart.ch/de/produkt/melitta-6769600-ventil-kaffeemaschine

Thanks again, you've helped me a lot!

Posted by: Schlawi February 11, 2024 10:44 pm

Great, good luck with the installation.

Bean2cup.org > Melitta > Melitta Avanza 600 / F270 drain valve replacement

#### www.bean2cup.org

back

Print